## Slide 1: Process Cycle Efficiency (PCE)

## Slide 2: Value Add – A Customer/User Perspective A Reminder
Customer Value Add
(CVA) Questions
Does the task add form, feature, or function to the process or service?
Does the task enable an advantage (reduced price, faster delivery, fewer defects)?
Would the user be willing to pay extra if he or she knew we were doing this task?
Example CVA Activities:
  Perform surgery
  Place mail in box
  Process patient
  Check-in guest
Non-Value Add (NVA)
Questions
If the user knew we were doing this, would they request that we eliminate the activity so we could reduce cost?
Does the task fit into either of the other two categories?
Can I eliminate or reduce this activity?
Typical NVA Activities:
  Question handling
  Document handling
  Inspecting
  Transporting/Moving
  Stocking/Storing
  All Rework Loops
  Signoffs
Non-Value Add-Required
(NVA-R) Questions
Does this task reduce owner financial risk?
Does this task support financial reporting requirements?
Would the process of producing the service break down if this task were removed?
Is this task required by law or regulation?
Typical NVA-R Activities:
  Taking an order
  Invoice processing
  IRS/OSHA/EPA reporting
  Internal Financial Reporting
  User Required Inspection

## Slide 3: Process Cycle Efficiency (PCE)
PCE is a measure of the relative efficiency in a process - it represents the percentage of value add time (changing form, fit, function) of a product down the critical path
It is calculated using:
PCE is the performance indicator of how efficiently the process is converting work-in-process into exits

## Slide 4: Process Cycle Efficiency (PCE)
World Class Cycle Efficiency Benchmarks*
Creative/Cognitive Processes | 5% | 25%
Transactional Processes | 10% | 50%
Batch Transfer Assembly | 15% | 35%
Continuous/One Piece Flow Assembly | 30% | 80%
* Based on experience with over 100 companies
Application
High-End PCE Goal
(World-Class PCE)
Low-End PCE Goal
Utilize ‘High-End PCE Goal’ if current process is greater than Low-End Goal but less than High-End Goal. Utilize ‘Low-End PCE Goal’ if current process is less than that goal. If current process is significantly less than Low-End Goal, shift decimal point of current PCE one digit to the right.

## Slide 5: Example: Calculating PCE
PLT = 5 days
Exit Rate =
20 Units/Day
WIP = Sum of All Work Within Physical Work Area = 100 Units
CVA =0.4 hrs
CVA =0.4 hrs
CVA =0.7 hrs
Our Example PCE is:
PCE = CVA Time / PLT
PCE = 1.5 hrs / 5 days
PCE = 4.0% (assume 7.5 hrs/day)
What is the Process Cycle Efficiency for the process below?
Process
1
Process
2
Process
3

## Slide 6: Refresher: PLT and PCE
Recall that:
Work-In-Process (WIP) = “Things in Process” – Orders, People In Queue, Documents, etc.
Exit Rate = The output of a process, expressed in units/time (equal to the rate of the time trap (constraint) operation)
Process Lead Time (PLT) = the time from release of a product into a process until it is completed
Customer Value Add Time (CVA Time) = the amount of time that value is actually being added to a product (the time that the customer is willing to accept)
PLT = WIP / Exit Rate
PCE = CVA Time / PLT
Process
Exit Rate
Work In Process
& CVA Time
Process Lead Time
Input

## Slide 7: The Value of Lead Time – Example 1
Process
Inputs
WIP
Lead Time
Process
WIP
Exits
You are planning the end-of-year holiday season work force needs for the European mail center. You estimate that there will be 1 million incoming items (packages, letters, and cards) each evening that need to be processed. There are currently 100 employees working at the mail center.
  Assuming the current work force can process 25,000 items per hour, how long will it take before the last item leaves the center?
  If all of the items need to be processed in no more than 8 hours, how many additional employees need to be hired?

## Slide 8: The Value of Lead Time – Example 2
Process
Inputs
WIP
Process Lead Time
Process
Work-In-Progress
Exits
A Central Issue Facility (CIF) processes approximately 100 Soldiers per day. Through value-stream mapping, it is determined the average value-add time for a Soldier is 30 minutes. This process is conducted over an 8 hour day.
Assuming this is a world class business process, what is the lead time for any given Soldier to be processed through the CIF? How many Soldiers should be in process at any given time?
Notes: 8

## Slide 9: Exercise: Calculate Process Cycle Efficiency (PCE)
Objective
Calculate the PCE for GGA's Budget Department
Instructions (Led by the Budget Director)
Calculate the Current PCE
Time = 15 Minutes
Notes: 9